## Slide 1: Open Cap vs Tracker
Kai Jen, Ian, Kevin

## Slide 2: Open Cap Setup
2 iPhone’s capturing at 60 frames per second.

## Slide 3: Tracker Setup
1 iPad capturing at 60 frames per second.
The squats were filmed perpendicular to the sagittal plane, facing the left side of the individual.

## Slide 4: Method – set up
Calibration: Followed OpenCap instructions.
Recording: Videos were captured with markers on the hip, knee, and ankle for tracker
Trials: Three squat trials were performed with hands crossed over the chest.
Filtering: 4th-order zero-lag Butterworth low-pass filter
Cutoff Frequency: Set at 6 Hz.
Event Definition:
Event 1: The hip joint position drops below the stance posture
  (calculated as the average of the first five frames).
Event 2: The hip joint position returns below the stance posture after Event 1.
Time Normalization: Each trial was resampled to 100 frames.
Knee Angle Calculation: Relative angles were used.
Knee flexion / extension

## Slide 5: Method – analysis data
Comparison
rms of the Max knee flexion-angle of each trail
  open cap vs tracker
  Within trails ( open can tracker)
ICC (ICC(2,1) - Two-Way Random, Absolute Agreement)

## Slide 6: Method – linear kinematics
Export csv data from OpenCap
  Vertical jump data
  Variables: position data of (X, Y, Z)
Process – python
  Interpolation: cubic polynomial method
  Filtering: 4th-order zero-lag Butterworth low-pass filter (cutoff = 6Hz)
  Linear velocity and acceleration : time derivative

## Slide 7: Maximum Knee Flexion Angle
Open Cap
Squat 1 = 89.79
Squat 2 = 87.21
Squat 3 = 82.56
Tracker
Squat 1 = 105.80
Squat 2 = 102.74
Squat 3 = 97.09

## Slide 8: Open Cap vs Tracker (squat 1)

## Slide 9: Open Cap vs Tracker Results

## Slide 10: Open Cap vs Tracker Results

## Slide 11: Open Cap vs Tracker Results

## Slide 12: Open Cap vs Tracker
RMS for knee flexion angle: 15.4°
ICC for squat 1: 0.74 (Moderate agreement)
ICC for squat 2: 0.85 (Good agreement)
ICC for squat 3: 0.87 (Good agreement)

## Slide 13: Open Cap RMS for Knee Flexion Angles
Squat 1 RMS = 2.32°
Squat 2 RMS = 2.16°
Squat 3 RMS = 2.68°
Average RMS = 2.39°

## Slide 14: Tracker RMS for Knee Flexion Angles
Squat 1 RMS = 3.03°
Squat 2 RMS = 1.86°
Squat 3 RMS = 3.44°
Average RMS = 2.78°

## Slide 15: Vertical Jump on Open Cap

## Slide 16: Key Take Aways
When comparing open cap to tracker, they seem to have good agreement and reliability (0.74-0.87).
The high RMS (15.4°) between the 2 devices could be due to the differences in tracked joint positions.
Overall, the RMS for each individual motion capture showed low variability for the squats.
  Open Cap average = 2.39°
  Tracker average = 2.78°

## Slide 17: Thank you
< - Link for the code – Please feel free to use