## Slide 1: Counter Movement Jump
Ian, Kai-Jen, Kevin, Nick

## Slide 2: Introduction
Vertical Jump is a key indicator of lower body strength and is used in many sport settings. This research focuses on how the task instruction can change the outcome of a vertical jump.
One participant was knowledgeable about the questions and goals and the other was blind and just given basic instruction
Verbal instructions may have implications to vertical jump outcome metrics

## Slide 3: Method
100 Hz by a 8-camera optical motion capture system
(Theia 3D, Theia Markerless Inc., Kingston, ON )
1200 Hz by 1 force plate
(Bertec Corp.; Columbus, OH, USA )

## Slide 4: Method
Two college participants
Participant 1 (in research group)
Participant 2 (not in research group)
(height: 1.79 .11 m; mass: 83.36kg 20.16kg)
Two vertical jumps for each participant
  First one: cued by “Jump as high as possible” (AHAP)
  Second one: cue by “Jump as fast as possible” (AFAP)

## Slide 5: Method
Data processes:
  Filter data: 4th zero lag Butterworth low pass filtering
    cutoff frequency = 6Hz for motion data / 20Hz for force plate data
  Calculate knee flexion / extension angle following the previous homework
  (relative angles)
  Calculate knee angular velocity with angle respect by the time interval
  Calculate jump height by impulse method
  Calculate impulse by integral
  Normalized ground reaction force (GRF) and impulse by body weight (BW)
Knee flexion / extension

## Slide 6: Method
Event setting
# START =
the start of the jump
(GRF < 95% BW )
# MIN_GRF_Y = minimum vertical GRF
# Back to BW =
GRF goes up to equal to the BW after min vertical GRF
# Botton point =
lowest point of the jump
( maximum knee flexion angle)
# Take Off =
GRF < 10% BW
# Touch Down =
GRF > 0.1 BW after take off

## Slide 7
Braking phase
Time interval (sec)

## Slide 8: Method – Report parameters
Kinematics
1. maximum knee flexion angle (degree)
2. max knee flexion angular velocity (degree / s)
Kinetics
1. max vertical GRF before take off (N/BW)
2. breaking impulse (J/BW)
3. propulsion impulse (J/BW)

## Slide 9: Kinematic Results (Participant 1)
 | AHAP | AFAP
Jump Height(m) | 0.43m | 0.41m
Max Knee Flexion Angle(degree) | 80.53° | 115.34°
Max Knee Flexion Velocity(degree / sec) | -230.95 deg/sec | -338.71 deg/sec
  “Jump as high as possible” (AHAP)
  “Jump as fast as possible” (AFAP)

## Slide 10: Kinetic Results (Participant 1)
 | AHAP | AFAP
Max Vertical GRF (N/BW) | 2.33 N | 2.81 N
Breaking Impulse (J/BW) | .16 J | .31 J
Propulsive Impulse (J/BW) | .65 J | .45 J
  “Jump as high as possible” (AHAP)
  “Jump as fast as possible” (AFAP)

## Slide 11: Time Series Results (participant 1)
  “Jump as high as possible” (AHAP)
  “Jump as fast as possible” (AFAP)
 | AHAP | AFAP
Unweight time (sec) | 0.53 | 0.38
Breaking time (sec) | 0.18 | 0.15
Propulsion time (sec) | 0.33 | 0.20
Flight time (sec) | 0.60 | 0.59
Total time (sec) | 1.45 | 1.17

## Slide 12: Kinematic Results (Participant 2)
 | AHAP | AFAP
Jump Height(m) | 0.24m | 0.22m
Max Knee Flexion Angle (degree) | 89.82° | 89.3°
Max Knee Flexion Velocity (degree / sec) | -263.42 deg/sec | -226.64 deg/sec
  “Jump as high as possible” (AHAP)
  “Jump as fast as possible” (AFAP)

## Slide 13: Kinetic Results (Participant 2)
 | AHAP | AFAP
Max Vertical GRF (N/BW) | 2.29 N | 2.29 N
Breaking Impulse (J/BW) | .09 J | .04 J
Propulsive Impulse (J/BW) | .51 J | .53 J
  “Jump as high as possible” (AHAP)
  “Jump as fast as possible” (AFAP)

## Slide 14
  “Jump as high as possible” (AHAP)
  “Jump as fast as possible” (AFAP)
 | AHAP | AFAP
Unweight time (sec) | 0.48 | 0.44
Breaking time (sec) | 0.15 | 0.12
Propulsion time (sec) | 0.28 | 0.27
Flight time (sec) | 0.45 | 0.43
Total time (sec) | 1.2 | 1.16
Time Series Results (participant 2)

## Slide 15: Results – Participant 1

## Slide 16
Results – Participant 2

## Slide 17: Results
When comparing the two groups of those who knew the outline of the study and those who only were given the instructions the comparisons are vastly different. In the group participants both variables led to vastly different results, while despite the differing instructions the out-group participant's two vertical jumps were almost identical
This brings to question if previous vertical jump experience as well as previous task knowledge influences counter movement jump outcomes.

## Slide 18: Potential Reasons for Results
Participant experience level
Understanding task instructions (may be related to experience level)
No warmup

## Slide 19: Future Research
Continue to look at task instruction and effects on CMJ metrics
Try different instruction cues to see if results differ

## Slide 20: Questions?